## Slide 1
Smart India Hackathon 2024
Problem statement ID:
SIH 1550
36313
Development of portable device (non-contact device) for measurement of eye pressure in glaucoma patients for usage at home.
Problem statement Title:
Theme:
MedTech / Bio Tech / HealthTech
PS Category:
Hardware
Team ID:
Team Name:
Aqueous
Hardware

## Slide 2
Tono_LITE
PROPOSED SOLUTION
Detailed Explanation :
COST-EFFECTIVE , PORTABLE ,LIGHT WEIGHT, NON-CONTACT Device
Measures Intra ocular pressure (IOP) up to 50 mmHg Accurately , Reliably with safety
How it Addresses the Problem :
Innovation and Uniqueness:
1. Central Corneal Thickness (CCT) factor applied output algorithm
Reflective property of cornea
4. Components meets the Medical ISO ,IEC ,ANSI std
9.Harmless significant Emitter 880nm
5. Device Final Price range 8k to 10k
Methods
Corneal hysteresis
2. Glaucoma identification using Low hysteresis value
3. Remote patient monitoring using IOT &DATA ANALYTICS
6. Bernoulli’s theorem to maintain Constant pressure
7. Reliable and precise IOP even after Corneal Surgery
8.Weight of the final Product is 750g
10.Optimized components for 50 mmHg
1.Even in low-cost ,it provides accurate results through ergonomic components
2.Portable and Light weight because of Miniature components
3.Non-contact due to Ocular response analyzer method

## Slide 3
Technical Approach
Hardware
IR Unit:
1.Harmless Power IR Emitter (880nm)
2. Photo-Diode (700-1100nm)
Response in Nano Seconds.
Controller Unit:
1.ESP 32 Wifi ,Bluetooth Development
2.Data Rate: 150Mbps
3.Frequency :2.4 GHz
Software
Dynamic Applanation Tonometry Algorithm +CCT +Corneal Hysteresis
IOT
Air-Puff Unit :
1.Air-Intaker
2.Pressure-Regulator
3.Solenoid-Valve
4.Round-Jet Nozzle
5.Connecting pipes
Display:
1.OLED module
2.Self Luminous
3.I2C protocol
Data on cloud
Remote monitoring

## Slide 4
Methodology & Process for implementation
Flow Chart / Images
35 Degree Angle
1
Inner-Schematic View
D= 30mm
IR Emitter
photodiode
Outer-Schematic View
2
Working:
Air-Pump
Pressure-Regulator
Solenoid-Valve
Nozzle
Produces 600mmHg
Regulates to 55mmHg
Works as gate
Outputs 50mmHg
Based On The Applanation Rate And Corneal Hysteresis ,IOP And Glaucoma Will Be Monitored.

## Slide 5
Feasibility & Viability
1. ANALYSIS OF THE CONCEPTUAL & TECHNICAL FEASIBILTY OF THE IDEA
2. WHY THE IDEA IS VIABLE?
Calibration Is The Highly Challenging ,By Testing And Simulation We Can Achieve The Good Calibration.
Regulatory compliance could slow down the market entry .
So , The Miniature Ocular Response Analyzer is HIGHLY FEASIBLE AND POSSIBLE IN REAL-TIME
Our Miniature Ocular Response Analyzer (TonoLite), measures the IOP by Corneal hysteresis and Central Corneal Thickness (CCT)
1.Air-Puff Unit :The Air-Pump ,Regulator ,Solenoid valve ,Nozzle effectively produces the amount of(50mmhg)
2. IR Unit :IR emitter and photodiode has high and large area of photosensitivity ,can reliably detect even small amount of reflection.
3. Controller and IOT: ESP32 module effectively perform all the above requirement.
1.Cost Effective – very lower than current market products.
2.User Friendly – portable and easy operation.
3.Medical standards – components satisfies ISO standards.
4.Strong market potential – medically highly impactful.
5.Technical Scalability– accurate and low maintenance.
6.Overall viability score – 85% from Gen-AI
3. POTENTIAL CHALLENGES
TR Level is 4

## Slide 6
Impacts & Benefits
1. Potential Impact on Target Audience
Glaucoma Patient
Diagnosing IOP
Often IOP changes , need to be Diagnosed even outside of clinical settings
Existing High Cost and Non-Portable and Contact Device
Tono_LITE
Helps patients proactively monitor their condition by using low cost and portable non-contact device, preventing disease progression through regular, at-home IOP checks.
Measures at 50 mmHg
Generally 80 million people will be impacted around the world by this device
2. Benefits of the Solution
Easy Accessibility
Preventative care
Low cost
Easy to use

## Slide 7
Research and References
Glaucoma Risk factors and Progression
- 1. Glaucoma Risk factor (analysis)
- 1. iCare home2 ​ 2. Keeler Pulsair
IR Emitter in medical applications
- 1. Infrared Emitter
Photodiode
IOP measurement
- 1. Measurement Method
​Drive Link - Essential Documents,3D Model & Circuit of the Device
Literature Review
- 1. ANSI
ANSI Z 136.1
- 1. Absorbance measurements
Measurement of light Reflection
- 1. Photo Detection Measurement
Constant Air Pressure Maintenance
- 1. Bernoulli’s Principle